## Slide 1
Toward a 400 Gb/s serial link
Project proposal • Cairo University, Faculty of Engineering
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
01
Model first. Verify the budgets.
Then design the hardware.
Student team: [add names]
Professor / supervisor: [add name]
8 October 2026
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Present the research question: can a paper-inspired MIMO-OFDM link be upgraded from about 224 to 400 Gb/s per lane with defensible converter, channel and clock requirements?

## Slide 2
Our team and the proposed project
A student research project spanning communications, circuits and digital design.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
02
Workstream | Proposed responsibility
Communication modeling | MATLAB link, BER/SER, channel and FEXT cancellation
Analog / converter design | ADC/DAC, clock, noise and process feasibility
Digital implementation | Fixed-point OFDM, MIMO equalization and RTL
System integration | Co-simulation, power/area estimates and final validation
Team members and role allocation: [to be completed by the team]
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Team names were not provided. Workstream roles below are proposed responsibilities, not assigned individuals. Each workstream should be coordinated by students with professor supervision.

## Slide 3
The research question
Can we reach 400 Gb/s per lane with realistic hardware constraints?
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
03
1 Understand and audit the published 224G architecture.
2 Use MATLAB to identify a conditional 400G operating point.
3 Replace ideal assumptions with measured and circuit-level evidence.
4 Implement the feasible design after the professor approves its scope.
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.

## Slide 4
How the link works
OFDM divides the signal into many tones; MIMO processing cancels lane-to-lane crosstalk.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
04
Part | Function
Transmitter | QAM symbols → OFDM / IFFT → cyclic prefix → DAC
Interconnect | Main signal path plus far-end crosstalk between lanes
Receiver | ADC → FFT → channel estimation → MIMO equalization
Evaluation | Recovered symbols → symbol and bit error measurements
Current phase: behavioral modeling and feasibility planning.
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Real OFDM uses Hermitian symmetry: 511 positive-frequency data tones with FFT1024. Two modeled lanes. Digital equalization estimates the channel matrix, including far-end crosstalk (FEXT). No FEC is implemented.

## Slide 5
224G: rate established; paper accuracy still open
The current model is not yet a full reproduction of the paper’s error performance.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
05
Metric | Current 224G model | Paper comparison
Gross rate / lane | 223.563 Gb/s | 224 Gb/s (rounded)
SER with cancellation | 7.432 × 10⁻⁵ | 1.4 × 10⁻⁵
Pre-FEC BER | 1.239 × 10⁻⁵ | 2.4 × 10⁻⁶
DAC / ADC clipping | 12.6 / 13.4 dB | 12.6 / 13.4 dB
Channel / FEXT and noise placement differ. Closing this gap is a project task.
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
224 result: docs/friend_channel_reproduction.md. Three seeds31,53,79, 5600 symbols per lane per seed, pooled103017600 bits; L1000. Paper targets from specs/224G_paper_specs.md. Current friend entry injects1.8mV noise after VGA; 400G verification puts noise before VGA. Imported channel has weaker FEXT than paper. Comparison therefore does not establish paper replication.

## Slide 6
The equation that sets the data rate
400G comes from the symbol rate and bit loading; BER tells us whether the data survives.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
06
R = Nused × log₂(M) × Fs / (NFFT + NCP)
Parameter | 224G starting point | 400G proposal
FFT / cyclic prefix | 1024 / 8 samples | 1024 / 8 samples
Data tones / modulation | 511 / 64-QAM (6 bits) | 511 / 64-QAM (6 bits)
DAC / ADC sample rate | 75.25 GS/s | 134.638 GS/s
Calculated gross rate | 223.563 Gb/s / lane | 400.000 Gb/s / lane
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
R=Nused*log2(M)*Fs/(NFFT+NCP). 511 tones, FFT1024, CP8. Rates are gross per lane, before training and FEC. Fs requirement for64QAM400 is134.637964774951GS/s.

## Slide 7
What must improve to support 400G
These budgets worked together in the model; they are not proven minimum hardware specifications.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
07
Requirement | Starting scalar budget | Tested 400G candidate
Sampling / Nyquist | 75.25 GS/s / 37.625 GHz | 134.638 GS/s / 67.319 GHz
Ideal ADC / DAC bits | 7 / 7 | 8 / 8
Channel loss at 40 GHz | 23 dB (synthetic anchor) | 5 dB (synthetic anchor)
RX noise before VGA | 1.8 mV RMS budget | 0.3 mV RMS
Jitter per TX / RX | 132.89 fs RMS | 22.282 fs RMS
DAC / ADC clipping | 12.6 / 13.4 dB | 12.6 / 13.4 dB
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Starting values are paper/current scalar budgets, not a circuit specification equivalence. Candidate synthetic channel loss anchor5dB@40GHz; full assumed frequency response matters. Absolute jitter22.28199fs for each independent TX/RX timing process. Ideal8-bit quantizers do not determine required real ENOB. Full scales1.0/.5Vpp remain unchanged. TX loading changes from-10.5..0 to-3.5..0dB; CHEST L200 in candidate.

## Slide 8
Raising the sample rate alone fails
A better converter alone is insufficient: channel loss, noise and jitter must improve together.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
08
400G screening change | Measured model BER
Original scalar budgets at the higher rate | 9.297 × 10⁻²
Only raise ideal converter resolution to 9 bits | 9.019 × 10⁻²
Also reduce channel loss and match TX loading | 1.263 × 10⁻³
Also reduce input noise to 0.3 mV | 5.921 × 10⁻⁴
Also reduce jitter to 22.282 fs | 0 observed in screening
Screening identifies bottlenecks. Independent long runs confirm the selected candidate.
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Screening data, seed401,1000 symbols/lane: BER original.0929705;9-bit-only.0901869;9bit pluslowloss5dB/matchedloading.00126288; lower noise.3mV .00059214; lowerjitter22.28fs gives zero observed in shortscreen. Finalcandidate8bit independently confirmed. Do not imply sequentialhardwareprototype results.

## Slide 9
400G: a conditional model result
Three independent runs confirm the 64-QAM candidate; 256-QAM needs further work.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
09
Chart: 
| 64-QAM bound | 256-QAM | 256-QAM lower noise
BER statistic / target | 0.012117 | 1.4682 | 1.1557
Comparison threshold | 1 | 1 | 1
64-QAM: 0 observed errors
103 million tested bits
Nominal 95% BER bound:
2.908 × 10⁻⁸
Paper BER: 2.4 × 10⁻⁶
Conditional on synthetic channel and ideal converters. Zero observed errors ≠ zero true BER.
The nominal confidence bound does not cover physical model uncertainty.
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Native editable chart shows BER statistic divided by paper comparison target2.4e-6.64QAM value is NOMINAL one-sided95% upper bound2.907981e-8, not observed BER;256 values are observed point estimates3.5236697e-6 and2.7737979e-6. Target series1. 64QAM zeroerrors103017600bits/17169600symbols.3seeds4314574795600dataOFDM/lane. Nominal bounds assumeindependentBernoullidecisions;OFDMcorrelation/modelerrornotbounded. NominalSERupper1.744788e-7 below1.4e-5. 256 rows fail both BER/SER comparisons.

## Slide 10
Which modulation should we pursue?
Prioritize 64-QAM for the next validation phase; keep 256-QAM as an alternative.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
10
Option | 64-QAM | 256-QAM
Sample rate for 400G | 134.638 GS/s | 100.978 GS/s
Nyquist coverage | 67.319 GHz | 50.489 GHz
Ideal converter resolution | 8 bits tested | 9 bits tested
Independent model result | Conditional pass | Comparison targets not met
Main challenge | Bandwidth, converter and clock | Tighter symbol separation / SNR
The tradeoff: lower modulation order needs more bandwidth; higher order needs cleaner signals.
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
256QAMstandard9idealbits,5dBanchor,.3mV,22.282fs;lowernoisevariant.1mV10fs. Pooled standardSER2.818936e-5 lower2.219038e-5. Both failpapercomparisons. Proposed choice subjectto professor approval.

## Slide 11
Can smaller transistors make this physical?
A smaller CMOS node may support integration and speed; it does not guarantee the link budgets.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
11
Public speed reference: imec reported a 175 GS/s, 7-bit ADC in 5 nm.
Our model uses ideal 8-bit converters: real ENOB / SNDR must be checked.
We need a PDK, analog bandwidth, clock and noise evidence before choosing a node.
Lower channel loss requires an interconnect improvement as well.
Reference: imec, 17 February 2026 • full source and limitations in speaker notes.
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Primary reference: https://www.imec-int.com/en/press/imec-unveils-7-bit-175gss-massively-time-interleaved-slope-adc-pairing-record-small-footprint (17Feb2026),5nmFinFET nominal7-bit175GS/s ADC. This establishes a public sampling-speed reference only: no claim its ENOB,inputbandwidth,jitter,swing orpower meetthiscandidate. NominalbitsvsENOB reference https://www.analog.com/en/resources/technical-articles/defining-and-testing-dynamic-parameters-in-highspeed-adcs-part-1.html. No PDK/circuit library supplied.

## Slide 12
Our plan for the whole project
Proceed through evidence gates; each phase produces a reviewable deliverable.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
12
Phase | Work and deliverable | Gate to the next phase
1 • Model and understand | Paper audit; 224G baseline; 400G budget report | Reproducible baseline and agreed targets
2 • Validate the link | Measured channel; converter, clock and noise models | Robust BER / SER with realistic impairments
3 • Design the hardware | AFE / ADC / DAC feasibility; fixed-point DSP / RTL | PVT, timing, power and area evidence
4 • Integrate and evaluate | Circuit–DSP co-simulation; prototype if available | End-to-end result and documented limitations
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Currentphase1isbehavioralmodeling/planning;candidateverificationcompletedconditionally,paperreproductionopen. Workplan proposed without claimingapprovedduration,budget,tapeoutorfabrication. Circuitphase needs PDKaccess andsupervisorapproval;siliconmeasurementonlyiffabricationavailable.

## Slide 13
What we need to verify next
Focus effort on the assumptions that can overturn the 400G result.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
13
Channel: measured THRU / FEXT, reach, material and connector response.
Converters and clock: ENOB vs frequency, noise, jitter and interleaving mismatch.
Digital chain: fixed-point errors, parallel throughput, timing, power and area.
System reliability: independent seeds, PVT corners, training and FEC overhead.
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
RealcomplexTHRU/FEXTcoverageatleast67.319GHzplusmarginrequired for64QAM;friendchannelmax50GHzinsufficient. Model jitter uses first-order spectral_linear derivative;validate broaderclockimpairments/aperture/phase noise. ADC inputnoisebeforeVGA. Additional independent runs and parameter/PVTsweeps, per-lane metrics required. No actualPDK,transistor circuit,layout,area/power validation exists.

## Slide 14
Decisions requested from the professor
Approve the research scope and the next validation phase.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
14
Agree on the target: 400 Gb/s per lane, gross rate or useful payload?
Approve 64-QAM as the primary path and define acceptable BER / FEC.
Select available process / converter resources and a realistic interconnect.
Set phase milestones, team responsibilities and implementation limits.
Proposal: continue from a verified behavioral candidate to a physically credible design.
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Approvalrequestisforresearchplan,notclaimofcircuitverified400G. Clarify perlanegrossvspayloadfirst; no FECimplemented. Keepfixedpaperclipping12.6/13.4. Approve64QAMasprimary400candidate,availablePDKandchanneldata, feasibleprojectresources/deliverables.

## Slide 15
Appendix • 400G gross is not 400G payload
Training and error-correction overhead must be included in the final speed requirement.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
15
Useful rate = gross rate × training efficiency × FEC code rate
Illustrative calculation | Rate / lane
Model gross rate | 400.00 Gb/s
With 2 training symbols per 200 data symbols | 396.04 Gb/s
Also assuming a 0.94 FEC code rate | 372.28 Gb/s useful payload
Example only: the training schedule and FEC scheme require approval and verification.
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Illustration only: two trainingOFDMsymbolsafter200datasymbols andFECrate.94,neitherverifiedFEC norfixedtrainingschedule.400*200/202=396.0396beforeFEC;times.94=372.2772payload. Toobtain400payloadsame assumptions64Fs144.664GS/s requiresnewlinkrun.

## Slide 16
Appendix • Evidence and reproducibility
Editable proposal based on the current repository results, not a new simulation run.
CAIRO UNIVERSITY | FACULTY OF ENGINEERING
16
Reference papers
G. Kim • MIMO OFDM with FEXT cancellation • IEEE TCAS-II, 2023
G. Kim • OFDM serial-link design-space exploration • IEEE OJCAS, 2022
Repository evidence
docs/400G_verification_for_doctor.md
results/400G_verification/pooled.csv and confirmation.csv
MATLAB: run_400G_verification; validate_phase1;
Notes: Project evidence: docs/400G_verification_for_doctor.md; results/400G_verification/pooled.csv, screening.csv, confirmation.csv. Results completed 8 October 2026, MATLAB R2026b. Research proposal: no silicon implementation claimed.
Paper: G.Kim, Far-EndCrosstalkCancellationWithMIMOOFDMfor>200Gb/sADC-BasedSerialLinks, IEEE TCAS-II70(1),81–85,Jan2023. G.Kim, DesignSpaceExplorationofSingle-LaneOFDM-BasedSerialLinksforHigh-SpeedWirelineCommunications,IEEEOpenJCircuitsSyst3,134–146,2022. LocalPDFsroot. MATLABsourcesrun_400G_verification.m;run_400G_cp_verification.m;run_400G_training_verification.m;validate_phase1.m. Current224docs/friend_channel_reproduction.md.